Name: Bayu Kanugrahan Luknanto
Position Applied: Robotics Application Engineer

PART A
Before performing mapping or navigation task, there are several checks that need to be made. The checks are:
- Robot’s assembly checks to see whether all the components have been assembled properly or not
- Robot’s power checks to see whether all the hardware get powered or not
- Robot’s actuators checks to see whether all actuation systems are working or not
- Robot’s sensor checks to see whether all sensors receive proper signal or not
- Communication checks between the robot and the ground control station.
- Fail-safe checks to see whether the fail-safe configuration is properly set or not (e.g. what should happen when it losses communication, what should happen when it has low battery level, etc)
- Software checks to see whether all modules are running or not (e.g. localization, mapping, etc)

PART B
related package: nav_waypoints

There are two controllers tested: Trajectory Rollout and Dynamic Window Approaches. The two controllers need to be tuned so that the robot can navigate well. In tuning the controllers, these parameters should be considered:
- Robot configuration parameters, such as maximum velocity and acceleration limit, must be set properly according to the robot specification. Because turtlebot3 is used, these parameters are set with respect to turtlebot3 specification.
- The desired goal tolerance should be set not to small. Otherwise, the robot will think that it never reach the desired goal and oscillate around the goal. To tune this parameter, the parameter is set a little bit large at first and then decrease it until before the robot starts to oscillate.
- Simulation time parameter. If it is set too low, it does not have sufficient time to obtain the optimal trajectory in a narrow passageway situation. Yet, setting it too high can burden the computational power of the robot. So, it is better to start low and see the robot’s performance. If the performance is not good, increase the simulation time. A value of 2.0 is good enough for turtlebot3.
Each controller has its own advantages and disadvantages. Dynamic Window Approaches is more efficient in terms of computation but might be under-performing when the robot has low acceleration limit. Trajectory Rollout is more expensive in terms of computation power but might be better when the robot has low acceleration limit. Also, from observing several simulations, Trajectory Rollout requires greater tolerance than Dynamic Window Approaches. That means Dynamic Window Approaches is more precise than Trajectory Rollout.

PART C
related package: path_sampler

Given a rosbag file which contains collection of points, the task is to sample N points such that the sampled points still represents the collection of points. To do this, the number of points in the rosbag must be known. Hence, rather than playing the rosbag using “rosbag play”, it is more efficient to directly read the rosbag. To directly read the rosbag, the rosbag file itself should be copied to the docker because the program will be run on the docker. Because docker-compose is going to be used, the copying process is done by putting the rosbag file to be sampled inside a specific folder, then performing the copy of the program and the rosbag file simultaneously.

Now, the sampling problem will be addressed. Because of possible noise on the dataset, it is necessary to perform filtering. A quite robust method in the presence of outlier is to take the median from the data. However, because there is quaternion data, taking median from the data is difficult, if not impossible. Another method that can be used is taking the average from the data. Because the shape of the sampled path needs to resemble the original path, moving average approach is taken. Again, taking average from quaternion is not straightforward, but still possible. According to this link: http://www.acsu.buffalo.edu/%7Ejohnc/ave_quat07.pdf, the average of quaternion is possible through this procedure.
Let Q=[ a_1 q_1, a_2 q_2, ..., a_n q_n] where a_i is the weight of ith quaternion and q_i is the ith quaternion being averaged (as a column vector). Therefore, Q is a 4 times N matrix.
The weighted average of the quaternion is the normalized eigenvector corresponding to the largest eigenvalue of QQ^T . If the weight is uniform, the average of the quaternion can be obtained.

Now that the filtering method has been addressed, the next problem is to determine how much data to be averaged. If the number of sample to be taken is a factor of the number of points in the original path, the solution is simply to divide the number of points in the original path by the number of sample. However, this is not the case. To deal with this, flooring the result is employed. Unfortunately, simply flooring the result might lead to ignoring points close to the end of the path Hence, before flooring the result of the division, the result of the division is multiplied by the sample index to get from which data to which data that should be averaged. After the multiplication, the result is floored. Below is an example of ten points with three samples.
1
2
3
4
5
6
7
8
9
10
Floor(10/3*1) = 3
Floor(10/3*2) = 6
Floor(10/3*3) = 10

Sample index 1

Sample index 2

Sample index 3

Now, the solution to the path sampling problem is completed. Given a rosbag file containing a trajectory to be sampled and the number of samples, the program will output two rosbag files: sampled_output.bag and combined_output.bag. The sampled_output file contains only the sampled points while the combined_output file contains the sampled points and the original trajectory. The purpose of the latter is to compare the original trajectory to the sampled trajectory.